## Slide 1: Digital Logic Design I CS1026
Paula.Roberts@scss.tcd.ie

## Slide 2
The inverter performs the Boolean NOT operation. When the input is LOW, the output is HIGH; when the input is HIGH, the output is LOW.
The Inverter
A
X
LOW (0) HIGH (1)
HIGH (1) LOW(0)
The NOT operation (complement) is shown with an overbar. Thus, the Boolean expression for an inverter is X = A.

## Slide 3
The Inverter
Example waveforms:
A
X
A
X
A group of inverters can be used to form the 1’s complement of a binary number:
Binary number
1’s complement
1 0 0 0 1 1 0 1
0 1 1 1 0 0 1 0

## Slide 4
The AND gate produces a HIGH output when all inputs are HIGH; otherwise, the output is LOW. For a 2-input gate, the truth table is
The AND Gate
The AND operation is usually shown with a dot between the variables but it may be implied (no dot). Thus, the AND operation is written as
X = A .B or X = AB.
0 0
0 1
1 0
1 1
0
0
0
1
A
B
X
A
B
X

## Slide 5
Example waveforms:
A
X
The AND operation is used in computer programming as a selective mask. If you want to retain certain bits of a binary number but reset the other bits to 0, you could set a mask with 1’s in the position of the retained bits.
The AND Gate
A
B
X
B
00000011
Example
If the binary number 10100011 is ANDed with the mask 00001111, what is the result?
A
B
X

## Slide 6
The OR gate produces a HIGH output if any input is HIGH; if all inputs are LOW, the output is LOW. For a 2-input gate, the truth table is
The OR Gate
The OR operation is shown with a plus sign (+) between the variables. Thus, the OR operation is written as X = A + B.
0 0
0 1
1 0
1 1
0
1
1
1
A
B
X
A
B
X

## Slide 7
Example waveforms:
A
X
The OR operation can be used in computer programming to set certain bits of a binary number to 1.
The OR Gate
B
Example
A
B
X
A
B
X
ASCII letters have a 1 in the bit 5 position for lower case letters and a 0 in this position for capitals. (Bit positions are numbered from right to left starting with 0.) What will be the result if you OR an ASCII letter with the 8-bit mask 00100000?
Solution
The resulting letter will be lower case.

## Slide 8
The NAND gate produces a LOW output when all inputs are HIGH; otherwise, the output is HIGH. For a 2-input gate, the truth table is
The NAND Gate
0 0
0 1
1 0
1 1
1
1
1
0
A
B
X
A
B
X
The NAND operation is shown with a dot between the variables and an overbar covering them. Thus, the NAND operation is written as X = A .B (Alternatively, X = AB.)

## Slide 9
Example waveforms:
A
X
The NAND gate is particularly useful because it is a “universal” gate – all other basic gates can be constructed from NAND gates.
The NAND Gate
B
Question
How would you connect a 2-input NAND gate to form a basic inverter?
A
B
X
A
B
X

## Slide 10
The NOR gate produces a LOW output if any input is HIGH; if all inputs are HIGH, the output is LOW. For a 2-input gate, the truth table is
The NOR Gate
0 0
0 1
1 0
1 1
1
0
0
0
A
B
X
A
B
X
The NOR operation is shown with a plus sign (+) between the variables and an overbar covering them. Thus, the NOR operation is written as X = A + B.

## Slide 11
Example waveforms:
A
X
The NOR operation will produce a LOW if any input is HIGH.
The NOR Gate
B
Example
When is the LED is ON for the circuit shown?
Solution
The LED will be on when any of the four inputs are HIGH.
A
B
X
A
B
X

## Slide 12
The XOR gate produces a HIGH output only when both inputs are at opposite logic levels. The truth table is
The XOR Gate
0 0
0 1
1 0
1 1
0
1
1
0
A
B
X
A
B
X
The XOR operation is written as X = AB + AB. Alternatively, it can be written with a circled plus sign between the variables as
X = A + B.

## Slide 13
Example waveforms:
A
X
Notice that the XOR gate will produce a HIGH only when exactly one input is HIGH.
The XOR Gate
B
Question
If the A and B waveforms are both inverted for the above waveforms, how is the output affected?
There is no change in the output.
A
B
X
A
B
X

## Slide 14
The XNOR gate produces a HIGH output only when both inputs are at the same logic level. The truth table is
The XNOR Gate
0 0
0 1
1 0
1 1
1
0
0
1
A
B
X
A
B
X
The XNOR operation shown as X = AB + AB. Alternatively, the XNOR operation can be shown with a circled dot between the variables. Thus, it can be shown as X = A . B.

## Slide 15
Example waveforms:
A
X
Notice that the XNOR gate will produce a HIGH when both inputs are the same. This makes it useful for comparison functions.
The XNOR Gate
B
Question
If the A waveform is inverted but B remains the same, how is the output affected?
The output will be inverted.
A
B
X
A
B
X

## Slide 16
Two major fixed function logic families are TTL and CMOS. A third technology is BiCMOS, which combines the first two. Packaging for fixed function logic is shown.
Fixed Function Logic
Dual in-line (DIP) package Small outline (SOIC) package

## Slide 17
Some common gate configurations are shown.
Fixed Function Logic

## Slide 18
Logic symbols show the gates and associated pin numbers.
Fixed Function Logic

## Slide 19
Data sheets include limits and conditions set by the manufacturer as well as DC and AC characteristics. For example, some maximum ratings for a 74HC00A are:
Fixed Function Logic

## Slide 20: Examples
Signal A and B are applied to a 2 i/p AND Gate. What is the o/p X

## Slide 21: Examples
Signals A, B and C are applied to a 3 i/p AND Gate. What is the o/p X

## Slide 22: Examples
For the 5 i/p waveforms shown determine the o/p if the 5 signals are ANDed. Determine the o/p if the 5 signals are ORed.

## Slide 23: Examples
Show that the o/p from the two gates shown are identical for the i/ps A and B

## Slide 24: Examples
Show that the o/p from the XNOR is as shown for the i/ps A and B