## Slide 1: Digital Logic Design I CS1026
Paula.Roberts@scss.tcd.ie

## Slide 2
In Boolean algebra, a variable is a symbol used to represent an action, a condition, or data. A single variable can only have a value of 1 or 0.
Boolean Addition
The complement represents the inverse of a variable and is indicated with an overbar. Thus, the complement of A is A.
A literal is a variable or its complement.
Addition is equivalent to the OR operation. The sum term is 1 if one or more if the literals are 1. The sum term is zero only if each literal is 0.
Example
Determine the values of A, B, and C that make the sum term of the expression A + B + C = 0?
Solution
Each literal must = 0; therefore A = 1, B = 0 and C = 1.

## Slide 3
In Boolean algebra, multiplication is equivalent to the AND operation. The product of literals forms a product term. The product term will be 1 only if all of the literals are 1.
Boolean Multiplication
Example
What are the values of the A, B and
C if the product term of A.B.C = 1?
Solution
Each literal must = 1; therefore A = 1, B = 0 and C = 0.

## Slide 4
Commutative Laws
In terms of the result, the order in which variables are ORed makes no difference.
The commutative laws are applied to addition and multiplication. For addition, the commutative law states
A + B = B + A
In terms of the result, the order in which variables are ANDed makes no difference.
For multiplication, the commutative law states
AB = BA

## Slide 5
Associative Laws
When ORing more than two variables, the result is the same regardless of the grouping of the variables.
The associative laws are also applied to addition and multiplication. For addition, the associative law states
A + (B +C) = (A + B) + C
For multiplication, the associative law states
When ANDing more than two variables, the result is the same regardless of the grouping of the variables.
A(BC) = (AB)C

## Slide 6
Distributive Law
The distributive law is the factoring law. A common variable can be factored from an expression just as in ordinary algebra. That is
AB + AC = A(B+ C)
The distributive law can be illustrated with equivalent circuits:
AB + AC
A(B+ C)

## Slide 7
Rules of Boolean Algebra
1. A + 0 = A
2. A + 1 = 1
3. A . 0 = 0
4. A . 1 = A
5. A + A = A
7. A . A = A
6. A + A = 1
8. A . A = 0
9. A = A
=
10. A + AB = A
12. (A + B)(A + C) = A + BC
11. A + AB = A + B

## Slide 8
Rules of Boolean Algebra
Rule 12, which states that (A + B)(A + C) = A + BC, can be proven by applying earlier rules as follows:
(A + B)(A + C) = AA + AC + AB + BC
= A + AC + AB + BC
= A(1 + C + B) + BC
= A . 1 + BC
= A + BC

## Slide 9
DeMorgan’s Theorem
The complement of a product of variables is equal to the sum of the complemented variables.
DeMorgan’s 1st Theorem
Applying DeMorgan’s first theorem to gates:

## Slide 10
DeMorgan’s Theorem
DeMorgan’s 2nd Theorem
The complement of a sum of variables is equal to the product of the complemented variables.
Applying DeMorgan’s second theorem to gates:

## Slide 11
Apply DeMorgan’s theorem to remove the overbar covering both terms from the
expression
DeMorgan’s Theorem
Example
Solution
To apply DeMorgan’s theorem to the expression, you can break the overbar covering both terms and change the sign between the terms. This results in

## Slide 12
Boolean Analysis of Logic Circuits
Combinational logic circuits can be analyzed by writing the expression for each gate and combining the expressions according to the rules for Boolean algebra.
Apply Boolean algebra to derive the expression for X.
Example
Solution
Write the expression for each gate:
Applying DeMorgan’s theorem and the distribution law:
C (A + B )
= C (A + B )+ D
(A + B )
X = C (A B) + D = A B C + D
X

## Slide 13
SOP and POS forms
Boolean expressions can be written in the sum-of-products form (SOP) or in the product-of-sums form (POS). These forms can simplify the implementation of combinational logic, particularly with PLDs. In both forms, an overbar cannot extend over more than one variable.
An expression is in SOP form when two or more product terms are summed as in the following examples:
An expression is in POS form when two or more sum terms are multiplied as in the following examples:
A B C + A B A B C + C D C D + E
(A + B)(A + C) (A + B + C)(B + D) (A + B)C

## Slide 14
SOP Standard form
In SOP standard form, every variable in the domain must appear in each term. This form is useful for constructing truth tables or for implementing logic in PLDs.
You can expand a nonstandard term to standard form by multiplying the term by a term consisting of the sum of the missing variable and its complement.
Example
Solution
Convert X = A B + A B C to standard form.
The first term does not include the variable C. Therefore, multiply it by the (C + C), which = 1:
X = A B (C + C) + A B C
= A B C + A B C + A B C

## Slide 15
POS Standard form
In POS standard form, every variable in the domain must appear in each sum term of the expression.
You can expand a nonstandard POS expression to standard form by adding the product of the missing variable and its complement and applying rule 12, which states that (A + B)(A + C) = A + BC.
Example
Solution
Convert X = (A + B)(A + B + C) to standard form.
The first sum term does not include the variable C. Therefore, add C C and expand the result by rule 12.
X = (A + B + C C)(A + B + C)
= (A +B + C )(A + B + C)(A + B + C)

## Slide 16
The Karnaugh map (K-map) is a tool for simplifying combinational logic with 3 or 4 variables. For 3 variables, 8 cells are required (23).
The map shown is for three variables labeled A, B, and C. Each cell represents one possible product term.
Each cell differs from an adjacent cell by only one variable.
Karnaugh maps

## Slide 17
Cells are usually labeled using 0’s and 1’s to represent the variable and its complement.
Gray code
Karnaugh maps
Ones are read as the true variable and zeros are read as the complemented variable.
The numbers are entered in gray code, to force adjacent cells to be different by only one variable.

## Slide 18
AB
AB
AB
AB
C C
Alternatively, cells can be labeled with the variable letters. This makes it simple to read, but it takes more time preparing the map.
Karnaugh maps
Read the terms for the yellow cells.
Example
Solution
The cells are ABC and ABC.

## Slide 19
1. Group the 1’s into two overlapping groups as indicated.
Read each group by eliminating any variable that changes across a boundary.
The vertical group is read AC.
K-maps can simplify combinational logic by grouping cells and eliminating variables that change.
Karnaugh maps
Group the 1’s on the map and read the minimum logic.
Example
B changes across this boundary
C changes across this boundary
Solution
The horizontal group is read AB.
+

## Slide 20
A 4-variable map has an adjacent cell on each of its four boundaries as shown.
Each cell is different only by one variable from an adjacent cell.
Grouping follows the rules given in the text.
The following slide shows an example of reading a four variable map using binary numbers for the variables…
Karnaugh maps

## Slide 21
X
Karnaugh maps
Group the 1’s on the map and read the minimum logic.
Example
1. Group the 1’s into two separate groups as indicated.
Read each group by eliminating any variable that changes across a boundary.
The upper (yellow) group is read as AD.
Solution
The lower (green) group is read as AD.
B changes
C changes
B changes
C changes across outer boundary

## Slide 22: Examples
Find the values of the variables that make each product term 1 and each sum term 0

## Slide 23: Examples
Apply De Morgan’s rules to each expression

## Slide 24: Examples
Calculate the o/p for each circuit below

## Slide 25: Examples
Draw the logic circuit represented by
X=A+B+C
X=ABC
X=AB+C
X=AB+CD

## Slide 26: Examples
Simplify the following Boolean expressions

## Slide 27: Examples
X=
Develop a truth table for

## Slide 28: Examples
Minimise using K-maps

## Slide 29: Examples
Minimise using K-maps

## Slide 30: Examples

## Slide 31: Examples