## Slide 1: Digital Logic Design I CS1026
Paula.Roberts@scss.tcd.ie

## Slide 2
Basic rules of binary addition are performed by a half adder, which has two binary inputs (A and B) and two binary outputs (Carry out and Sum).
Half-Adder
The inputs and outputs can be summarized on a truth table.
A
B
S
Cout
The logic symbol and equivalent circuit are:
A
B
S
Cout
S

## Slide 3
Full-Adder
By contrast, a full adder has three binary inputs (A, B, and Carry in) and two binary outputs (Carry out and Sum). The truth table summarizes the operation.
A full-adder can be constructed from two half adders as shown:
A
B
S
Cout
S
A
B
S
Cout
S
A
B
Sum
Cout
Cin
A
B
S
Cout
S
Cin
Symbol

## Slide 4
Complete Logic circuit for Full Adder

## Slide 5
Full-Adder
A
B
S
Cout
S
A
B
S
Cout
S
Example
Solution
For the given inputs, determine the intermediate and final outputs of the full adder.
1
1
0
1
0
The first half-adder has inputs of 1 and 0; therefore the Sum =1 and the Carry out = 0.
The second half-adder has inputs of 1 and 1; therefore the Sum = 0 and the Carry out = 1.
The OR gate has inputs of 1 and 0, therefore the final carry out = 1.
1
0
1
Sum
Cout

## Slide 6
Full-Adder
A
B
S
Cout
S
A
B
S
Cout
S
1
1
0
1
0
1
0
1
Sum
Cout
Notice that the result from the previous example can be read directly on the truth table for a full adder.

## Slide 7
Parallel Adders
Full adders are combined into parallel adders that can add binary numbers with multiple bits. A 4-bit adder is shown.
A
B
S
Cout
Cin
A
B
S
Cout
Cin
A
B
S
Cout
Cin
A
B
S
Cout
Cin
A1 B1
S1
C0
S2
S3
S4
C1
C2
C3
C4
A2 B2
A3 B3
A4 B4
The output carry (C4) is not ready until it propagates through all of the full adders. This is called ripple carry, delaying the addition process.

## Slide 8
Parallel Adders
The logic symbol for a 4-bit parallel adder is shown. This 4-bit adder includes a carry in (labeled (C0) and a Carry out (labeled C4).
The 74LS283 is an example. It features look-ahead carry, which adds logic to minimize the output carry delay. For the 74LS283, the maximum delay to the output carry is 17 ns.
Binary number A
Binary number B
Input carry
4-bit sum
Output carry
1
2
3
4
1
2
3
4
1
2
3
4
C0
C4
S

## Slide 9: Devise a Truth Table for a 4-Bit Parallel Adder
What are the inputs?
What are the outputs?

## Slide 10: Truth Table for a 4-bit adder
Cn-1 | An | Bn | ∑n | Cn
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 11
Comparators
The function of a comparator is to compare the magnitudes of two binary numbers to determine the relationship between them. In the simplest form, a comparator can test for equality using XNOR gates.
Example
Solution
How could you test two 4-bit numbers for equality?
AND the outputs of four XNOR gates.
A1
B1
A2
B2
A3
B3
A4
B4
Output

## Slide 12
Comparators
IC comparators provide outputs to indicate which of the numbers is larger or if they are equal. The bits are numbered starting at 0, rather than 1 as in the case of adders. Cascading inputs are provided to expand the comparator to larger numbers.
Outputs
A1
A0
A2
A3
B1
B0
B2
B3
Cascading inputs
COMP
A = B
A < B
A > B
A = B
A < B
A > B
0
0
3
3
A
A
The IC shown is the 4-bit 74LS85.

## Slide 13
Comparators
IC comparators can be expanded using the cascading inputs as shown. The lowest order comparator has a HIGH on the A = B input.
Outputs
A1
A0
A2
A3
B1
B0
B2
B3
COMP
A = B
A < B
A > B
A = B
A < B
A > B
0
0
3
3
A
B
A5
A4
A6
A7
B5
B4
B6
B7
+5.0 V
COMP
A = B
A < B
A > B
A = B
A < B
A > B
0
0
3
3
A
B
LSBs
MSBs

## Slide 14
Decoders
A decoder is a logic circuit that detects the presence of a specific combination of bits at its input. Two simple decoders that detect the presence of the binary code 0011 are shown. The first has an active HIGH output; the second has an active LOW output.
A1
A0
A2
A3
X
Active HIGH decoder for 0011
A1
A0
A2
A3
X
Active LOW decoder for 0011

## Slide 15
Decoders
Assume the output of the decoder shown is a logic 1. What are the inputs to the decoder?
Question

## Slide 16
Decoders
IC decoders have multiple outputs to decode any combination of inputs. For example the binary-to-decimal decoder shown here has 16 outputs – one for each combination of binary inputs.

## Slide 17: Question For the input shown, what is the output?

## Slide 18
Decoders
A specific integrated circuit decoder is the 74HC154 (shown as a 4-to-16 decoder). It includes two active LOW chip select lines which must be at the active level to enable the outputs. These lines can be used to expand the decoder to larger inputs.
CS2
A1
A0
A2
A3
CS1
X/Y
EN
74HC154

## Slide 19
Decoders
BCD-to-decimal decoders accept a binary coded decimal input and activate one of ten possible decimal digit indications.
A1
A0
A2
A3
Example
Solution
Assume the inputs to the 74HC42 decoder are the sequence 0101, 0110, 0011, and 0010. Describe the output.
All lines are HIGH except for one active output, which is LOW. The active outputs are 5, 6, 3, and 2 in that order.

## Slide 20
BCD Decoder/Driver
Another useful decoder is the 74LS47. This is a BCD-to-seven segment display with active LOW outputs.
The a-g outputs are designed for much higher current than most devices (hence the word driver in the name).
BCD inputs
Outputs to seven segment device
GND
VCC
BCD/7-seg
BI/RBO
BI/RBO
LT
RBI
LT
RBI
74LS47

## Slide 21
BCD Decoder/Driver
Here the 7447A is an connected to an LED seven segment display. Notice the current limiting resistors, required to prevent overdriving the LED display.

## Slide 22
BCD Decoder/Driver
Blanked
Blanked
The 74LS47 features leading zero suppression, which blanks unnecessary leading zeros but keeps significant zeros as illustrated here. The BI/RBO output is connected to the RBI input of the next decoder.
Depending on the display type, current limiting resistors may be required.

## Slide 23
BCD Decoder/Driver
Blanked
Blanked
Decimal point
Trailing zero suppression blanks unnecessary trailing zeros to the right of the decimal point as illustrated here. The RBI input is connected to the BI/RBO output of the following decoder.

## Slide 24
Encoders
An encoder accepts an active logic level on one of its inputs and converts it to a coded output, such as BCD or binary.
The decimal to BCD is an encoder with an input for each of the ten decimal digits and four outputs that represent the BCD code for the active digit. The basic logic diagram is shown. There is no zero input because the outputs are all LOW when the input is zero.
A1
A0
A2
A3
1
2
3
4
5
6
7
8
9

## Slide 25
Encoders
A1
A0
A2
A3
Example
Solution
Show how the decimal-to-BCD encoder converts the decimal number 3 into a BCD 0011.
The top two OR gates have ones as indicated with the red lines. Thus the output is 0011.
1
2
3
4
5
6
7
8
9
0
0
0
0
0
0
0
0
1
0
0
1
1

## Slide 26
Encoders
The 74HC147 is an example of an IC encoder. It is has nine active-LOW inputs and converts the active input to an active-LOW BCD output.
This device is offers additional flexibility in that it is a priority encoder. This means that if more than one input is active, the one with the highest order decimal digit will be active.
Decimal input
BCD output
GND
VCC
HPRI/BCD
74HC147

## Slide 27
A multiplexer (MUX) selects one data line from two or more input lines and routes data from the selected line to the output. The particular data line that is selected is determined by the select inputs.
Multiplexers
Two select lines are shown here to choose any of the four data inputs.
Data
select
Data
inputs
Data
output
D1
D0
D2
D3
S1
S0
Question
Which data line is selected if S1S0 = 10?
D2
1
0

## Slide 28
A demultiplexer (DEMUX) performs the opposite function from a MUX. It switches data from one input line to two or more data lines depending on the select inputs.
The 74LS138 was introduced previously as a decoder but can also serve as a DEMUX. When connected as a DEMUX, data is applied to one of the enable inputs, and routed to the selected output line depending on the select variables. Note that the outputs are active-LOW as illustrated in the following example…
Demultiplexers
74LS138
Data select lines
Enable
inputs
Data outputs

## Slide 29
Determine the outputs, given the inputs shown.
Demultiplexers
Example
74LS138
Data select lines
Enable
inputs
Data outputs
A
0
Y
0
Y
1
Y
2
Y
3
Y
4
Y
5
Y
6
Y
7
A
1
A
2
G
1
G
2A
G
2B
LOW
LOW
The output logic is opposite to the input because of the active-LOW convention. (Red shows the selected line).
Solution

## Slide 30
Parity Generators/Checkers
Parity is an error detection method that uses an extra bit appended to a group of bits to force them to be either odd or even. In even parity, the total number of ones is even (including the parity bit); in odd parity the total number of ones (including the parity bit) is odd. Used in keyboards, PCI bus, RAID Arrays.
11010011
S with odd parity =
S with even parity =
01010011
Example
The ASCII letter S is 1010011. Show the parity bit for the letter S with odd and even parity.
Solution

## Slide 31
Parity Generators/Checkers
The 74LS280 can be used to generate a parity bit or to check an incoming data stream for even or odd parity.
Checker: The 74LS280 can test codes with up to 9 bits. The even output will normally be HIGH if the data lines have even parity; otherwise it will be LOW. Likewise, the odd output will normally be HIGH if the data lines have odd parity; otherwise it will be LOW.
Generator: To generate even parity, the parity bit is taken from the odd parity output. To generate odd parity, the output is taken from the even parity output.
74LS280
Data inputs
S Even
S Odd

## Slide 32: Examples
Determine the Full Adder o/ps for the following i/ps
A=1, B=0, Cin=0
A=0, B=0, Cin=1
A=0, B=1, Cin=1
A=1, B=1, Cin=1

## Slide 33: Examples
The input waveforms shown are applied to a 2 bit adder. Draw the waveform diagrams for the Sum and o/p Carry

## Slide 34: Examples

## Slide 35: Examples
A0
A1
B0
B1
COMP
A
A=B
B
Draw the o/p waveform A=B

## Slide 36: Examples

## Slide 37: Examples
A1
A0
A2
A3
B1
B0
B2
B3
Vcc
COMP
A = B
A < B
A > B
A = B
A < B
A > B
0
0
3
3
A
A
For the 4 bit comparator in the Figure, plot each o/p waveform for the i/p shown

## Slide 38: Examples
For each set of binary inputs to the comparator, calculate the o/p
A=1100 B=1001
A=1000 B=1011
A=0100 B=0100

## Slide 39: Examples
Show the decoding logic for each of the following codes if an active high (1) o/p is required
1101
1000
11011
11100
101010
111110
000101
1110110

## Slide 40: Examples
Determine the o/p of this MUX
D0=1, D1=1, D2=1, D3=0,S0=0, S1=1
Solution

## Slide 41: Examples
The waveforms shown are applied to the 4 bit parity logic. Determine the o/p waveform. How many times does even parity occur and how is it indicated. The timing diagram includes 8 bit times.

## Slide 42: Examples